## Slide 1: ECE 337 Project Canny Edge Detection Final Presentation
Oluwatosin Adeosun, Sukhyun Hong,
Eric Nielsen, Jiyuan Zhao

## Slide 2: Project Overview
Edge detection using Canny algorithm
  Useful feature in image processing
  Highlights key features in images
ASIC implementation using pipelining
  Large amount of processing power needed
  Optimized for speed
Interfacing with 9 off-chip SRAMs
Input/output bitmap images
Four main functional blocks
  Image smoothing
  Gradient and magnitude calculation
  Directional non-maximal suppression
  Hysteresis thresholding

## Slide 3: System Level Diagram
Input Image
(Bitmap, 512x512 pixels)
9 Off-Chip SRAMs
(Cypress, CY7C1018DV33)
Canny Edge Detection Chip
Output Image
(Bitmap, 512x512 pixels)
Python Script
9 Address Lines (19 bit)
1 Off-Chip SRAM
(Cypress, CY7C1018DV33)
Python Script
9 Data Lines (8 bit)
Read Enable / Mem Init
Address Line (18 bit)
Data Line (8 bit)
Write Enable /
Mem Clear /
Mem Dump
Clk N_Rst Start

## Slide 4: Canny Edge Detection Flow Chart
Image Smoothing Block (Gaussian)
Magnitude Calculation Block
Horizontal & Vertical Gradient Calculation Block
Directional Non-Maximal Suppression Block
Hysteresis Thresholding
Input Image
Data
Output Image Data

## Slide 5: Architecture Diagram

## Slide 6: Layout
Core Utilization: 99.97%
Dimensions: 6.29mm x 6.27mm
Layout Critical Path Delay: 11.579 ns
Synthesis Critical Path Delay:
8.81 ns
Budgeted Critical Path Delay:
10.2 ns

## Slide 7: Success Criteria
Success Criteria | Points | Status
The design can successfully interface with the off-chip SRAM module (both read and write capabilities). | 1 | In Progress
The Gaussian block of the design operates correctly on original image data. | 1 | Achieved
The Gradient/Magnitude block of the design operates correctly on blurred image data. | 1 | Achieved
The Suppression block of the design operates correctly on the blurred pixel magnitude data. | 1 | Achieved
The Hysteresis block of the design operates correctly on the suppressed pixel data. | 1 | Achieved
The complete design is able to produce an output bitmap image with the edges in the original image accurately detected. | 3 | In Progress

## Slide 8: Gaussian Test Results
Expected
Actual

## Slide 9: Gradient/Magnitude Test Results
Expected
Actual

## Slide 10: Suppression Test Results
Expected
Actual

## Slide 11: Overall Test Results
Expected
Actual

## Slide 12: Conclusions
Challenges
  Design of interface with off-chip SRAM
  Pipelined data flow approach
    Design of buffers/data lines
    Timing at image edges
Alternate design approaches
  Fewer off-chip SRAMs
    Slower performance
    Much smaller chip size
  Integrate Python functionality into test-bench for easier operation
Possible improvements
  Support for multiple image sizes
  Auto-calculation of hysteresis thresholds

## Slide 13: Questions?

## Slide 14: Supporting Slides

## Slide 15: Image Smoothing (Gaussian)

## Slide 16: Gradient/Magnitude Calculation
x5

## Slide 17: Directional Non-Maximal Suppression

## Slide 18: Hysteresis Thresholding

## Slide 19: Main Controller RTL Diagram

## Slide 20: Main Controller State Diagram (Summary)

## Slide 21: Area & Timing Budgets
Block Name | Gate/FF Count | Area (um2) | Total Path Delay (ns) | Target Clock Period (ns)
Gaussian (slide 6) | 1,944 | 2,527,200 | 5.2 | 10
Gradient/Mag (slide 7) | 3,432 | 3,220,800 | 6.2 | 10
Directional Non-Maximal Suppression (slide 8) | 3,480 | 3,600,00 | 3.2 | 10
Hysteresis Thresholding (slide 9) | 113 | 203,550 | 1.6 | 10
Main Controller and Timer (slide 11) | 106 | 224,700 | 10.2 | 10
Total Core Dimensions:
3,091x3,091 um2
Total I/O Padframe Dimensions:
2,805x2,805 um2 (98 I/O pads)